## Slide 1: Trex自动化测试
Byzoro.com

## Slide 2: Agenda
TRex基本介绍
安装和运行
运行模式

## Slide 3: 测试工具需求
费用：
  购买费用、使用和维护成本
性能和功能需求
标准化
可扩展性：
  购买、自研、开源

## Slide 4: Trex功能性能
支持高达200Gb/s的流量测试，大流量 20mpps (1G线速1.488mpps)需要网卡及CPU支持
支持时延和抖动
支持NAT/PAT自动学习
支持L4~L7
状态和无状态
轻易产生stateless traffic stream
支持stream并发
支持更改报文字段范围
支持Continuous/Burst/Multi-burst support
支持console/GUI
支持每条流的统计
虚拟设备：AWS/Laas/ESXi 低性能设备比如桌面电脑和笔记本

## Slide 5: Avalanche与TRex的比较
网卡
Intel I350
Inter 82599
Inter X710
Mellanox ConnectX-4
Cisco1300 series
VMXNET/VMXNET3
E1000

## Slide 6: 安装
CentOS/RHEL 7.6, 64-bit kernel (not 32-bit) (Recommended) — This is the only working option for ConnectX-4.
  [bash]>uname –m
mkdir –p /opt/trex
cd /opt/trex
wget --no-cache http://trex-tgn.cisco.com/trex/release/latest
tar -zxvf latest
历史版本：https://trex-tgn.cisco.com/trex/release
[bash]>uname -m x86_64

## Slide 7: 运行TRex
检查网卡接口自环功能正常，建议使用相同NUMA获得最佳性能
配置文件/etc/trex_cfg.yaml
[bash]>sudo ./dpdk_setup_ports.py -s
[bash]>cp cfg/simple_cfg.yaml /etc/trex_cfg.yaml
[bash]>sudo ./dpdk_setup_ports.py -i
[bash]>sudo ./dpdk_setup_ports.py -t
更多信息：
https://trex-tgn.cisco.com/trex/doc/trex_manual.html#_script_for_creating_config_file

## Slide 8: Stateless模式
1、Service mode 简单基于端口的一些测试模式，如ARP, PING
2、命令行交互，需要特定的py脚本
3、纯Python接口编写的py脚本，可直接执行

## Slide 9
[bash]>sudo ./t-rex-64 -f cap2/dns.yaml -c 4 -m 1 -d 10

## Slide 10: stateless交互
服务器端：
sudo ./t-rex-64 -i --cfg /etc/trex2.yaml
客户端：
./trex-console
stateless模式下包模板在/opt/trex/v2.28/stl这个目录下

## Slide 11: Stateless流定义:scapy
1 from trex_stl_lib.api import *
2 import argparse
4
5 class STLS1(object):
7 def create_stream (self):
8 return STLStream(
9 packet =
10 STLPktBuilder(
11 pkt = Ether()/Dot1Q(vlan = 1100)/Dot1Q(vlan = 1110)/Dot1Q(vlan = 1120)/IP(src="16.0.0.1",dst="48.0.0.1")/
12 UDP(dport=53,sport=1025)/(1000*'x')
13 ),
14 mode = STLTXCont())
15
16 def get_streams (self, tunables, **kwargs):
17 parser = argparse.ArgumentParser(description='Argparser for {}'.format(os.path.basename(__file__)),
18 formatter_class=argparse.ArgumentDefaultsHelpFormatter)
19 args = parser.parse_args(tunables)
20 # create 1 stream
21 return [ self.create_stream() ]
24 # dynamic load - used for trex console or simulator
25 def register():
26 return STLS1()

## Slide 12: Stateless流定义:scapy
# UDP header
Ether()/IP(src="16.0.0.1",dst="48.0.0.1")/UDP(dport=12,sport=1025)
# UDP over one vlan
Ether()/Dot1Q(vlan=12)/IP(src="16.0.0.1",dst="48.0.0.1")/UDP(dport=12,sport=1025)
# UDP QinQ
Ether()/Dot1Q(vlan=12)/Dot1Q(vlan=12)/IP(src="16.0.0.1",dst="48.0.0.1")/UDP(dport=12,sport=1025)
#TCP over IP over VLAN
Ether()/Dot1Q(vlan=12)/IP(src="16.0.0.1",dst="48.0.0.1")/TCP(dport=12,sport=1025)
# IPv6 over vlan
Ether()/Dot1Q(vlan=12)/IPv6(src="::5")/TCP(dport=12,sport=1025)
#Ipv6 over UDP over IP
Ether()/IP()/UDP()/IPv6(src="::5")/TCP(dport=12,sport=1025)
#DNS packet
Ether()/IP()/UDP()/DNS()

## Slide 13: 在脚本中使用trex
ssh连接
ssh连接
TREX
T9600
Port0
Port1
1/43
1/44
自动化脚本

## Slide 14: 在脚本中使用trex
建立连接句柄
Log Connecting to Trex client
${trex} Connect SSH to Device ${trex_ip} username=${trex_username} password=${trex_password}
Set Suite Variable ${trex}
Log start trex server
${trex_svr} Connect SSH to Device ${trex_ip} alias=H_trex_svr username=${trex_username} password=${trex_password}
Start Trex Server ${trex_svr}
Stop Trex Server ${trex_svr}
Log upload traffic file to target trex server ${trex_traffic}
${ret} Execute Shell Command on ${trex} command=rm -rf ${trex_traffic}; mkdir -p ${trex_traffic}
Put Directory trex ${TEMPDIR}${/}${log}

## Slide 15: 在脚本中使用trex：statefull
662 ${trex_sum}= Operation Send Trex Traffic ${trex} traffic_template=${trex_traffic}/dns.yaml
663 ... cfg_file=${trex_traffic}${/}trex_cfg.yaml
664
665 ${int1_stats}= Fetch Interface Stats Detail ${dut} interface=${int_d0t0}
666 ${int2_stats}= Fetch Interface Stats Detail ${dut} interface=${int_d0t1}
667
668 Log Check interfaces counters to match expectation
669 Should Be Equal as Integers ${trex_sum}[port0_opackets] ${int1_stats}[Received Good Packets]
670 Should Be Equal as Integers ${trex_sum}[port0_ipackets] ${int1_stats}[Transmitted Good Packets]
671 Should Be Equal as Integers ${trex_sum}[port1_opackets] ${int2_stats}[Received Good Packets]
672 Should Be Equal as Integers ${trex_sum}[port1_ipackets] ${int2_stats}[Transmitted Good Packets]

## Slide 16: 在脚本中使用trex：stateless
3577 Log send packets
3578 Start Trex Server ${trex_svr}
3579 Log start trex-console
3580 Execute Shell Command on ${trex} command=cd ${trex_dir};./${trex_console}
3581 Execute Shell Command on ${trex} command=clear -a
3582 Execute Shell Command on ${trex} command=start -f ${trex_traffic}${/}vlan_tc_fun_020.py -p ${trex_port0_id}
3583 Sleep 5s
3584 Log stop trex traffic
3585 Execute Shell Command on ${trex} command=stop
3586 ${trex_sum}= Fetch Trex Console Stats ${trex}
3587 Exit Trex Console ${trex}
3588
3589 ${int1_stats}= Fetch Interface Stats Detail ${dut} interface=${int_d0t0}
3590 ${int2_stats}= Fetch Interface Stats Detail ${dut} interface=${int_d0t1}
3591 Should Be Equal as Integers ${trex_sum}[port0_opackets] ${int1_stats}[Received Good Packets]
3592 Should Be Equal as Integers ${trex_sum}[port0_ipackets] ${int1_stats}[Transmitted Good Packets]
3593 Should Be Equal as Integers ${trex_sum}[port0_opackets] ${int2_stats}[Transmitted Good Packets]

## Slide 17: 在脚本中使用trex：抓包
389 Log start capturing on port 1
390 Execute Shell Command on ${trex} command=service -p ${trex_port1_id} timeout=40s
391 #${ret} Execute Shell Command on ${trex} command=capture record start --rx ${trex_port1_id} --limit 2000 -f udp and dst 53 # timeout=40s
392 ${ret} Execute Shell Command on ${trex} command=capture record start --rx ${trex_port1_id} --limit 3000
393 ${match} ${capture_id} Should Match Regexp ${ret} Capturing ID is set to '(\\d+)'
394 Execute Shell Command on ${trex} command=clear -a
395 Execute Shell Command on ${trex} command=start -f ${trex_traffic}${/}mob_7_1_1_nested_vlan.py -d 30 -m 500 -p ${trex_port0_id}
396 Sleep 20s
397 Log stop trex traffic
398 Execute Shell Command on ${trex} command=stop
399 Execute Shell Command on ${trex} command=capture record stop --id ${capture_id} -o ${trex_traffic}${/}trex_capt.pcap
400 ${trex_sum}= Fetch Trex Console Stats ${trex}
401 Execute Shell Command on ${trex} command=service --off
402 Exit Trex Console ${trex}
403
404 ${int1_stats}= Fetch Interface Stats Detail ${dut} interface=${int_d0t0}
405 ${int2_stats}= Fetch Interface Stats Detail ${dut} interface=${int_d0t1}
406
407 Should Be Equal as Integers ${trex_sum}[port0_opackets] ${int1_stats}[Received Good Packets]
408 Should Be Equal as Integers ${trex_sum}[port0_ipackets] ${int2_stats}[Received Good Packets]
409 Should Be Equal as Integers ${trex_sum}[port0_opackets] ${int2_stats}[Transmitted Good Packets]

## Slide 18: 图形接口

## Slide 19: 图形接口